Real Time Executive Interface Definition

DRAFT 2.1

Prepared by:

MOTOROLA Microcomputer Division and

Software Components Group

Abstract:

This specialization denies a basic set of functions that constitute the Real Time Executive Interface Definition. Draft 2.1 is for public review, MOTOROLA/SCG retain the right to modify this definition as appropriate during implementation. Draft 2.1 will be submitted to the VITA technical committee no later than 01/25/88.

PRELIMINARY

REAL TIME EXECUTIVE INTERFACE DEFINITION

DISCLAIMER

This RTEID specification is being proposed to be used as the basis for formal standardization by the VME International Trade Association (VITA). However, since the standardization process has just begun, any standard resulting from

this document might be different from this document. Any Product designed to this document might not be compatible with the final standard. No responsibility is assumed for such incompatibilities and no liability is assumed for any product built to conform to this document.

While considerable effort has been expended to make this document

comprehensive, reliable, and unambiguous, it is still being published in preliminary form for public study and comment.

This document is prepared by Motorola Inc., Microcomputer Division. The

design and development of RTEID is a joint effort of Motorola Inc.,

Microcomputer Division and Software Components Group, Inc. Interest in the RTEID is welcomed and encouraged any technical questions, suggestions or

comments may be directed to:

Motorola Inc.

Microcomputer Division Dept: RTEID

2900 South Diablo Way Tempe, Arizona 85282 Tel: (602)438-3500

Fax: (602)438-3581 
Tlx: 4998071 (MOTPHE)

Software Components Group, Inc. 4655 Old Ironsides Drive

Santa Clara, California 95054 
Tel: (408)-437-0700

Fax: (408)727-0904

Tlx:	757697 (softcom)

REVISION RECORD

Issue	Revision Description	Date

1	Initial version. Internal Only.	051L3 /87

2	Added semaphores and debug management.	06/01/87

3	Preliminary Draft, limited distribution.	06/17/87

4	Design review of SCG's comments.	07/24/87

5	SCG/MOT Technical review.	08/20/87

8	SCG/MOT Technical review.	088/87

7	SCG/MOT Technical review.	09/14/87

8	SCG/MOT Technical review for Draft 2.1	12/14/87

9	Added Debug Extensions for Draft 2.1	12/22/87

10	Added I/O Interface for Draft 2.1	01/15/88

11	Removed Debug Extensions from Draft 2.1	01/22/88

12	Final Draft 2.1 submitted to VITA	01/25/88'

13

TABLE OF CONTENTS

Fri

Page

1. INTRODUCTION	1

1.1	Overview	1

1.2	Definitions	1

1.3	Typedefs and Structures	1

2. Basic System Services	2

3. EXECUTIVE FACILITIES	3

3.1	Task Management	7

3.1.1	T—CREATE	8

3.1.2	TDENT	10

3.1.3	T_START	11

3.1.4	T_RESTART	13

3.1.5	T_DELETE	15

3.1.6	T_SUSPEND	16

3.1.7	T_RESUME	17

3.1.8	T_SETPRI	18

3.1.9	T_MODE	19

3.1.10 T_GETREG	21

3.1.11 T—SETREG	23

3.2	Message, Event, and Signal Management	25

3.2.1	Message Manager	25

3.2.2	Event Manager	26

3.2.3	Signal Manager	27

3.2.4	Data Structures for Message Management	28

3.2.5	Q_CREATE	29

3.2.6	Q_IDENT	31

3.2.7	Q_DELETE	32

3.2.8	Q_SEND	33

3.2.9	Q_URGENT	34

3.2.10 Q_BROADCAST	38

3.2.11 Q_RECEIVE	37

3.2.12 EV_SEND	39

3.2.13 EV_RECEIVE	40

3.2.14 AS_CATCH	42

3.2.15 AS—SEND	44

3.2.18 AS—RETURN	45

3.3	Semaphore Management	46

3.3.1	SM_CREATE	47

3.3.2	SM_MENT	49

3.3.3	SM_DELETE	50

3.3.4	SM_P	51

3.3.5	SM_V	53

3.4	Time Management	54

3.4.1	Timebuf Structure	55

3.4.2	TM_SET	56

3.4.3	TM_GET	_57

108

3.4.4	TM_WKAFTER	58

3.4.5	TM_WKWHEN	59

3.4.8	TM_EVAFTER	60

3.4.7	TM_WKWHEN	61

3.4.8	TM_CANCEL	62

3.4.9	TM_TICK	63

3.5	Interrupt Handling	64

3.5.1	L_RETURN	65

3.8	Fatal Errors	68

3.8.1	K_FATAL	67

3.7	Memory Management	68

3.7.1	Region Manager	68

3.7.2	Partition Manager	69

3.7.3	RN_CREATE	70

3.7.4	RN_IDENT	72

3.7.5	RN_DELETE	73

3.7.6	RN_GETSEG	74

3.7.7	RN_RETSEG	76

3.7.8	PT_CREATE	77

3.7.9	PT_IDENT	79

3.7.10 PT_DELETE	80

3.7.11 PT_GETBUF	81

3.7.12 PT_RETBUF	82

3.8	MMU Management	83

.3.8.1	Segments vs. Sections	83

3.8.2	Regions		83

3.8.3	Partitions	83

3.8.4	MM_L2P	85

3.8.5	MM_P2L	86

3.8.8	MI/L_PMAP	87

3.8.7	MM_UNMAP	89

3.8.8	MM_PREAD	90

3.8.9	MM_PWRITE	91

3.8.10 MM_PTCREATE	92

3.9	Dual-ported Memory	94

3.9.1	M_EXT2INT	95

3.9.2	M_NT2EXT	96

4. I/O INTERFACE	97

4.1	Driver Properties	97

4.2	Data Structures	97

4.2.1	Driver Address Table	98

4.2.2	Device Data Area Table	98

4.3	Device Initialization	99

4.4	Parameter Passing	99

4.5	I/O Interface in C Language	99

4.6	I/O Interface in Assembly Language	100

4.7	Driver Interface in Assembly Language	100

4.8	Error Handling	101

4.9	I/O Interface Routines in C Language	101

4.9.1	INIT	102

4.9.2	OPEN	103

4.9.3	CLOSE	104

4.9.4	READ	105

4.9.5	    WRITE	106

4.9.6    CNTRL	107

4.10 Driver Interface in C Language

1. INTRODUCTION

1.1 Overview

This document is intended to serve the following major purposes:

• To serve as a reference source for the definition of the external interfaces to services that are 
	provided by all Real Time Executive environments. This includes source-code interfaces and 
	run-time behavior as seen by an application-program. It does not include the details of how

the kernel implements these functions.

• To serve as a complete definition of Real Time Executive external interfaces, so that application source-code that conforms to these interfaces, will execute as defined in all Real Time 
	Executive environments. It is assumed that source-code is recompiled for the proper target

hardware. The basic objective is to facilitate the writing of applications-program source-code that is directly portable across all Real Time Executive implementations.

This document describes the basic set of functionality that makes up the Base System. This functionality has been structured to provide a minimal, standalone run-time environment for application-programs originally written in a high-level language, such as C.

Other extensions to this Base System will be defined as a continuing effort to produce this standard Real Time Executive Run Time Environment.

It is anticipated that all conforming systems must support the source code interfaces and runtime behavior of the Base System. A system may conform to some, none, or all of the extensions.

1.2 Definitions

Executive	That portion of software that constitutes the kernel or performs

Specific services on behalf of programs tasks.

Real Time Executive	Same as executive.

Node	A processor within a multiprocessor system configuration.

Local node	The processor within a multiprocessor system configuration on

Which the current operation is being executed.

Remote node	A processor within a multiprocessor system configuration on

Which the current operation is not being executed.

Target	The destination remote node in a multiprocessor system

Configuration.

1.3 Typedefs and Structures

For ease of documentation, the following typedefs are used in this document.

typedef	unsigned int	uint;	/* 32-bit unsigned integer $/

typedef	void	(*ptf)();	/* pointer to a function that returns nothing */

LIST OF TABLES

TABLE 1. Directives	3

TABLE 2. Directive Usage	5

2.	Basic System Services

The Basic System Services is intended to support a minimal run-time environment for executable applications. The Basic System Services defines a set of Real Time Executive components needed by applications-programs. This basic set would be supported by any conforming system. It defines each component's source-code interface and run-time behavior, but does not specify its implementation. Source-code interfaces described are for the C language.

While only the run-time behavior of these components is supported by the Basic System Services, the source-code interfaces to these components are defined because an objective of the Real Time Executive Interface Definition is to facilitate application-program source-code portability across all Real Time Executive implementations. It is assumed that an application-program targeted to run on a system that provides only the Basic System Services (a run-time environment) would be compiled on a system supporting software development.

Real Time Executive Interface Definition	January 22, 1988

3.	EXECUTIVE FACILITIES

The facilities of the executive have been grouped by function, and are discussed in the following

paragraphs.

TABLE 1. Directives

Name	Input Parameters	Output Parameters

t_create	name	superstk	userstk	priority	lags	&tid

Lident	name	node	&tid

t_start	tid	saddr	mode	argp

t_sestart	tid	argp

t_delete	tid

t_suspend	tid

t_resume	tid

t_setpri	tid	priority	&ppriority

Mode	mode	mask	&pmode

t_getreg	tid	regnum	&regval

t_setreg	tid	regnum	regval

q_create	name	count	flags	&qid

q_ident	name	node	&qid

q_delete	qid	,

q_send	qid	buffer

q_urgent	qid	buffer

q_broadcast	qid	buffer	&count

_q_receive	qid	buffer	flags	timeout

ev_send	tid	event

ev_receive	eventin	flags	timeout	&eventout

as_catch	asraddr	mode

as_send	tid	signal

as_return

sm_create	name	count	lags	&smid

sm_ident	name	node	&smid

sm_delete	smid

sm_p	amid	flags	timeout

sm_v	amid

tm_set	timebuf

tm_get	timebuf

tm_wkafter	ticks

tm_wkwhen	timebuf

tm_evafter	ticks	event	&tmid

tm_ev-when	timebuf	event	&tmid

tm_cancel	tmid

tm_tick

Lreturn

k_fatal	errcode